## Slide 1: FTC wiring instructions with modern robotics
FTC Electronics 2017

## Slide 2: Power distribution module (PDM)
It is the brain of the robot
1. The black and red ports are called Anderson connectors, they give power to the motors.
2. The USB ports at the back give commands to each motor. (Order matters)
3. The black switch is the power switch to the robot
4. The yellow tab is the fuse that protects the electronics
5. Connect to the battery
6. This mini –USB port connect to the phone
3
2
1
4
5
6

## Slide 3: Motor controller
Each motor controller controls two motors
1. The Anderson connectors that says motor 1 and 2 connect directly to the motors
2. The Anderson that says 12V connect to the Anderson ports on the PDM
3. The mini-USB port at the back connect to the USB ports on the PDM
4. The small port that says ENC 1 and 2 connect to the encoders on the motor if there is any
1
2
3
4

## Slide 4: Configure the robot
Launch
Launch the FTC app on the phone >- click the three-dots button >- Configure Robot >- New >- Scan
Plug
Plug the motor controllers into the PDM one at a time and click scan each time
Name
When you see the motor appear on the phone screen, name it exactly as the variable name in the program