## Slide 1: Setup the phones
FTC 2017

## Slide 2: Phone Setup
1. Make sure Airplane mode and Wi-Fi are both on
2. Open the FTC apps on the Robot Controller (RC) and Driving Station (DS) phone
3. DS: Settings >- Connect with Robot Controller >- select it
RC: ACCEPT
4. Verify the following:
DS shows it is connected to RC; RC network name displayed on DS
RC shows connected to DS; “connected, active”

## Slide 3: Programming Mode
RC: three dots >- Programming Mode
Windows 10 PC: WIFI >- the name that matches the RC >- enter password and connect
Launch Chrome on your computer >- enter the IP address displaying on the RC screen i.e. something like “192.168.49.1:8080”
Click “Create New Op Mode” and enter a name for this mode
When you are done programming, click “Save Op Mode”
RC: click the back arrow at the bottom left to exit Programming Mode

## Slide 4: OP Mode
1. Check the back of your game controller (GC) to make sure it is in “X” position
2. Connect the GC to the DS with cables
3. Press “Start” + “A” for the driver and “Start” + “B” for the operator
4. Select an Op Mode and click “Init”
5. Click start to start and stop to stop